## Slide 1
SQI Pipeline Update
What changed, why, and where we landed with Mark & Rutendo
Lab Meeting Update — Lupita

## Slide 2
Why We Changed Things
Tried moving to a simpler window-level pipeline — filter, calculate PI, normalize the whole window, and classify it good/bad directly. No beat segmentation.
Ran it on real data and almost everything came back “good.” Two problems turned up:
The window-level check was only looking at clipping — a pretty lenient check on its own
PI was blowing up to hundreds/thousands of percent on some windows because it was calculated off the filtered signal — the bandpass filter strips the DC baseline, so AC/DC stops meaning anything
</>
Code snippet
e.g. old clipping-only classify_window(), or compute_perfusion_index() on the filtered signal

## Slide 3
Getting Realigned with Mark & Rutendo
Flagged both issues — Mark clarified two things that changed the plan:
We still need beat-to-beat comparison happening, not just one check on the whole window
Normalization should happen per beat, not per window — closer to our original pipeline than the window-only version
New pipeline (next slide) got Mark's sign-off, with one open note: he's not fully sold on using an unfiltered window for PI, but didn't have a clean way around it without detrending messing with the filter — so we're moving forward and revisiting later if needed.
</>
Code snippet
e.g. normalize_single_beat() — per-beat normalization

## Slide 4
Approved Pipeline
Signed off by Mark — this is what's currently implemented
Filter + PI
Bandpass filter window; PI from the RAW window signal
→
Segment Beats
Valley-to-valley detection on the filtered signal
→
Normalize Beat
Per-beat, 0–1 scale
→
Compare to Template
DTW, correlation, MAD, clipping
→
Classify Beat → Window
Window is bad if >30% of beats are bad
→
Export + Summarize
CSV per window → %Good / %Bad windows
Raw PPG → 10-second windows → (each window goes through the steps below)

## Slide 5
Implementation + Results
Implemented and running across Day 2 / 3 / 4 recordings.
33.12%
Good Windows
66.88%
Bad Windows
Fully reproducible — reran it and got the exact same split, so the pipeline itself is deterministic (nothing random going on).
</>
Code snippet
e.g. run_beat_comparison() / classify_beat()

## Slide 6
Open Issue: PI Outliers
About 116 windows have extreme PI values.
Traced 105 of those to one specific channel — Unpolarized_A_Green (hardware channel C5) — where the raw signal itself has near-zero amplitude in those windows.
Looks more like a hardware/sensor issue on that channel than a pipeline bug, but wanted to flag it before assuming that.
</>
Code snippet
e.g. affected channel's raw signal plot / compute_perfusion_index() output

## Slide 7
Open Issue: Threshold Retuning
Beat comparison switched from raw-amplitude beats to normalized (0–1) beats, so a few thresholds (sqi_lambda, min_template_sqi, max_mad) tuned for the old scale were basically dead weight on the new one.
Pulled real percentile distributions from ~43,000 actual beats and retuned those three thresholds to match.
Reran with the new numbers — overall split barely moved (33.03% / 66.97% vs. 33.12% / 66.88%) — so we reverted back to the original numbers rather than carry non-standard values. Reasoning is documented in the code.
</>
Code snippet
e.g. BeatSQIConfig defaults, before vs. after the retune

## Slide 8
Open Questions for Mark & Rutendo
Is the Unpolarized_A_Green (C5) PI issue a hardware/sensor thing we should exclude or flag, or is there a processing fix worth trying?
clipping_sqi values cluster tightly (roughly 0.55–0.94, median around 0.82) right around our 0.80 cutoff, for both good and bad beats. Worth rethinking whether the threshold or the underlying clipping formula needs adjusting?